## Slide 1
Remaining Useful Life Estimation
of Turbofan Engines Using Machine Learning
Felix Ikokwu · Hunter Antal | Lakehead University
• Predict cycles remaining before engine failure
• NASA C-MAPSS FD001 dataset
• Models compared: Random Forest, MLP, LSTM
Notes: Welcome everyone. This project asks a simple question: given sensor readings from a jet engine, how many cycles does it have left? We tested three models of increasing complexity to find out.

## Slide 2
Dataset & Problem
HUNTER 1/5
NASA C-MAPSS FD001
• ~100 engines, run-to-failure
• 21 sensors + 3 operational settings per cycle
• Training: full histories | Test: partial
Problem
• Supervised regression — predict RUL (cycles)
• RUL capped at 125 (healthy region)
• Split by engine ID — no data leakage
Notes: The dataset simulates turbofan engines degrading until failure. Each row is one operational cycle with 24 raw features. We cap RUL at 125 because before that point engines show no degradation signal. Engine IDs are kept separate between train and test to prevent leakage.

## Slide 3
Data Preprocessing
HUNTER 2/5
Feature Selection
• 9 features removed (low variance / low correlation)
• 15 features retained
Normalization
• Z-score: mean = 0, std = 1
• Prevents any feature dominating training
Windowing (LSTM)
• 30-cycle sliding windows
• RF & MLP flatten to a 450-dim vector
Notes: Three preprocessing steps. Feature selection removes noise. Normalization ensures fair training. Windowing gives the LSTM temporal context — it sees the last 30 cycles at once, rather than just the current cycle.

## Slide 4
Model Architectures
HUNTER 3/5
BASELINE
Random Forest
• Ensemble of decision trees
• 1 M params | 52 M FLOPs
INTERMEDIATE
MLP
• 3 hidden layers: 128 → 64 → 32
• BatchNorm + Dropout | 18 K params
BEST
LSTM
• 128-unit recurrent layer
• Preserves 30-cycle temporal order
• 83 K params | 22.6 B FLOPs
Notes: Three models of increasing complexity. Random Forest is our baseline — powerful but treats every cycle independently. MLP adds nonlinear transformations but still uses a flat input. LSTM is the only model that actually sees time — it processes 30 cycles in sequence.

## Slide 5
Evaluation Framework
HUNTER 4/5
Accuracy Metrics
• MAE — avg error in cycles
• RMSE — penalises large errors
• R² — variance explained (0–1)
Residual & Cost
• Residual = Actual − Predicted
• Overprediction = engine seems healthier than it is → dangerous
• Asymmetric loss penalises overprediction 50% harder (α = 1.5)
• Efficiency: parameter count & FLOPs
Notes: We care most about RMSE and R² for overall accuracy. But residual direction matters too — if we overestimate RUL we might delay maintenance on an engine that's about to fail. That's why we use asymmetric loss in the final LSTM: wrong in the dangerous direction costs more.

## Slide 6
Random Forest — Results
FELIX 1/5
12.38
MAE (test)
17.18
RMSE (test)
0.612
R² (test)
• Solid baseline — captures nonlinear feature relationships
• Compresses predictions at high RUL (early degradation) — underestimates severity
• Residual variance grows as engine approaches failure
• Hyperparameter tuning plateaus at RMSE ≈ 19.6 — structural limit, not a tuning issue
Notes: Random Forest is a strong starting point. It handles nonlinearity well. But it sees each cycle as an isolated snapshot — it has no idea what happened 10 cycles ago. That's why it struggles early in degradation when the signal is subtle and slow-building. More trees or deeper trees don't help — the bottleneck is the flat input, not the model complexity.

## Slide 7
MLP — Results
FELIX 2/5
12.07
MAE (test)
16.89
RMSE (test)
0.625
R² (test)
• Marginal improvement over RF in error metrics
• Tighter clustering around the diagonal vs. RF
• Test R² drops from 0.792 → 0.625 — generalisation limited by flat input
• Architecture [64, 128, 64] + LR 0.0005 was optimal
Notes: MLP adds learnable nonlinear transformations on top of the flat window. It does improve slightly, and the scatter plot looks a bit tighter. But the validation-to-test drop in R² tells us it's not generalising well to new engines. The root cause is the same as RF: no temporal structure in the input.

## Slide 8
LSTM — Results
FELIX 3/5
10.34
MAE (test)
14.76
RMSE (test)
0.754
R² (test)
• Best model — explicitly models temporal degradation sequences
• Substantially lower RMSE vs. RF and MLP on both val and test
• Narrower residual distribution — fewer extreme errors
• Val → test R² drop of only 0.14 pts (RF/MLP: ~0.17)
Notes: LSTM is a clear winner. By processing 30 cycles in order it can detect gradual drift that a single-cycle model would miss. The smaller val-to-test drop tells us it generalises better to engines it's never seen. This makes sense — temporal patterns of degradation are more universal than any single-point feature snapshot.

## Slide 9
Model Comparison
FELIX 4/5
Metric
Random Forest
MLP
LSTM
RMSE (val / test)
19.58 / 17.18
18.95 / 16.89
13.35 / 14.76
R² (val / test)
0.778 / 0.612
0.792 / 0.625
0.898 / 0.754
MAE (val / test)
14.01 / 12.38
13.50 / 12.07
9.21 / 10.34
Parameters
~1 M
18 K
83 K
FLOPs (test)
52 M
456 M
22.6 B
Notes: This table tells the full story. LSTM leads on every accuracy metric. What's interesting is the efficiency angle: RF has a million parameters but cheap inference. LSTM has 83K parameters but expensive sequential computation — 22 billion FLOPs. For a safety-critical maintenance system, the accuracy gain is worth the compute cost.

## Slide 10
Optimisation & Conclusions
FELIX 5/5
Best LSTM Config
• Hidden = 256 | Sequence = 75 cycles
• Dropout = 0.4 | Asymmetric loss (α = 1.5)
• ReduceLROnPlateau scheduler
• RMSE 13.33 | R² 0.839 | 62.4% within 10 cycles
Takeaways
• Temporal modelling drives accuracy — LSTM > MLP > RF
• More non-temporal complexity doesn't close the gap
• Asymmetric loss reduces dangerous overpredictions
• Future: attention, ensembling, multi-condition datasets
Notes: After selecting LSTM we ran a 150-configuration random search to tune it. The biggest wins came from longer sequences (75 vs 30 cycles) and asymmetric loss. The key conclusion: the ability to model time is what matters. If you can only pick one thing to improve a predictive maintenance model, add temporal structure.